Paravel Systems
APPLICATION NOTE 006
Configuring USB HID-Based Touchscreens on CentOS 5.5

SCOPE
This application note details the procedures for configuring USB HID-based touch-screens and -monitors (such as the ELO 'Intellitouch' touch monitors) on CentOS 5.5.

PROCEDURE
Required Packages
Install the following packages (available in the Paravel-Broadcast repository):
touchcal
touchmon

Modify X11 Configuration
If there is not already an InputDevice section for the mouse in the X11 configuration file in '/etc/X11/xorg.conf', add one as follows:

Section "InputDevice"
        Identifier "Mouse0"
        Driver "mouse"
        Option "Buttons" "9"
        Option "Device" "/dev/input/mouse0"
EndSection

and add the following line to the ServerLayout section:

InputDevice "Mouse0" "CorePointer"

If a section for the mouse already exists, change the Device entry to be /dev/input/mouse0.

When finished making changes to '/etc/X11/xorg.conf', restart the X server by logging out and then back in.

Hardware Connections
Connect the touchscreens to be configured to the system.

Calibrate
Run the calibration program (in System->Calibrate Touchscreen) and follow the on-screen instructions.

Modify X11 Configuration (again)
Add the following lines to the X11 configuration file in '/etc/X11/xorg.conf':

Section "InputDevice"
        Driver "touchmon"
        Identifier "Touchscreen0"
        Option "Device" "/dev/input/js0"
        Option "ScreenNo" "0"
        Option "AlwaysCore" "yes"
EndSection
and add the following line to the ServerLayout section:

InputDevice "Touchscreen0" "SendCoreEvents"

When finished making changes to '/etc/X11/xorg.conf', restart the X server by logging out and then back in.

This completes the procedure.

REVISION HISTORY
Mon 24 January 2011 – Fred Gleason <fredg@paravelsystems.com>
Initial document creation.