Paravel Systems
APPLICATION NOTE 009
Configuring Rivendell's Cue Output on Axia Element Consoles

SCOPE
This application note details the procedures for configuring Rivendell's 'Cue' output to work with the 'External Preview' function on an Axia Element console.

PREREQUISITES
1. An Axia Element console (both PowerStation and StudioEngine based).
2. Rivendell v2.5.5 or later, utilizing the LiveWire AoIP driver or AudioScience ASI6x85 adapter.

OVERVIEW
GPIO lines in LiveWire are organized into bundles of five lines, with each bundle being associated with a particular LiveWire source number. The specific function of each line within a bundle varies depending upon the type of device being controlled. A set of tables breaking down the line functions can be found in the manual for each LiveWire-compliant console.

PROCEDURE
1. Configure External Preview on one or more Element show profiles
  1. Open a web browser and enter the IP address of the Element Power Supply / PowerStation unit
  2. Create a Source Profile for the LiveWire source to be used for Rivendell Cue output of type Computer Player.
  3. Go to the Show Profiles section and select the desire show profile, the click the Monitor section link.
  4. In the General Monitor Settings section, set the Source ID for EXTERNAL preview dropdown list to the source profile created for Rivendell Cue.
  5. In the Control Room Monitor Options section, note the value of the GPIO Channel for CR Monitor setting.
  6. Repeat above procedure for other desired show profiles.
  7. Reload any modified show profile on the Element.
2. Configure Virtual GPIO (ASI6x85 card)
  1. Open a web browser and enter the IP address of the ASI6x85 card.
  2. Click the GPIO link to open the Virtual GPIO Configuration screen.
  3. Choose an unused line in the Ports table and enter the GPIO Channel for CR Monitor setting from the Element profile noted above (step 1-5) in the Channel column. Enter Element CR Monitor in the Name column. Make a note of the row number.
  4. Touch Apply.
3. Configure Virtual GPIO (LiveWire AoIP Driver)
  1. Open the driver configuration.
  2. In the Destinations section, set one of the GPO controls to the GPIO Channel for CR Monitor setting from the Element profile noted above (step 1-5). Make a note of the row number.
  3. Touch Save.
4. Configure GPIO driver in Rivendell
  1. Open RDAdmin->ManageHosts->[host-name]->Switchers/GPIO.
  2. Touch Add
  3. Make a note of the new matrix number.
  4. In the Switcher Type dropdown list, select LiveWire LWRP GPIO.
  5. Touch OK to open the Edit Switcher dialog.
  6. Enter the address of the ASI6x85 card or the multicast interface address of the LiveWire AoIP driver in the IP Address field, and select V in the Layer dropdown list, then touch OK.
  7. Close RDAdmin.
5. Create Macro Carts in Rivendell
  1. Open RDLibrary, then touch Add. Select Macro for New Cart Type and Element Preview On for New Cart Title and then touch OK.
  2. Touch the Add button and enter the following macro cart code 'GO <matrix> <line> 1 0!' , where value of <matrix> is the matrix number of the GPIO driver (from step 4) 3 above). The value for <line> is calculated by taking the GPIO row number (from step 2) 3 or 3) 2 above), multiplying it by five and then adding two. Touch OK and then OK again.
  3. Repeat step 2., this time titling the cart Element Preview Off and using the code 'GO <matrix> <line> 0 0!'.
  4. Close RDLibrary
6. Configure Cue Output in Rivendell.
  1. Open RDAdmin->ManageHosts->[host-name].
  2. In the Cue Output section, enter the appropriate Card and Port values for the desired LiveWire output stream.
  3. In the Start Cart field, enter the number of the Element Preview On macro cart from step 5) 1 above. In the Stop Cart field, enter the number of the Element Preview Off macro cart from step 5) 3.

Rivendell's Cue Output should now be configured correctly.

REVISION HISTORY
Mon 17 Mar 2014 – Fred Gleason <fredg@paravelsystems.com>
Initial document creation.